## Slide 1: Robot Car File Structure
Arduino nano main
Stepper core functions
Nano servo core functions
Electromagnet core functions
IR core functions
Bluetooth core functions
Nano ping sensor core functions
Arduino uno main
Drive core functions
Ping sensor servo core functions
Car ping sensor core functions

## Slide 2: Core Functions in Folder “Arduino_uno_main”
Arduino_uno_main.ino
  Contains setup() and loop()
  Users should place custom code here
Drive_core_functions.ino
  _mForward()
    Sets car in constant forward motion
  _mBack()
    Sets car in constant backward motion
  _mLeft()
    Sets car in constant pivot to the left
  _mRight()
    Sets car in constant pivot to the right
  _mStop()
    Stops the car
Car_ping_sensor_core_functions.ino
  _distanceTest()
    Returns the distance in front of the ping sensor (what units??)
Ping_sensor_servo_core_functions.ino
  _setServoAngle(int angle)
    Sets the angle of the servo controlling the car’s ping sensor. Specify an angle 0 through 180 degrees. 0 degrees is all the way to the right

## Slide 3: Core Functions in Folder “Arduino_nano_main”
Arduino_nano_main.ino
  Contains setup() and loop()
  Users should place custom code here
  Eventually, when the code to talk between Arduinos is created, all custom code will be on the Arduino_uno_main.ino
Electromagnet_core_functions.ino
  _electromagnetOn()
  _electromagnetOff()
Stepper_core_functions.ino
  _moveStepsNow(which motor, numSteps)
    If numSteps given is positive, stepper motor will turn clockwise; if negative, counterclockwise
    Motor executes code immediately (without advancing the main loop until the motor has reached its final position)
    Code is contained to the function (don’t need additional elements in main loop)
    Number of steps in one rotation is about 4076
  _moveStepsNonBlocking(which motor, numSteps)
    Same functionality as _moveStepsNow, but requires more understanding & changes to loop(); doesn’t hold up loop()—allows more simultaneous commands
Stepper_core_functions.ino, (cont.)
  _incrementAngleNow(which motor, angle)
    User specifies angle; function translates this to steps; global variable stores error from desired angle (exact angles not always possible due to resolution); when movements are made, function accounts for previous position in the calculation of the move to the new position
    Moves immediately, holding up the Arduino_nano_main.ino loop() to do so
  _incrementAngleNonBlocking(which motor, angle)
    Same as _incrementAngleNow(), but non-blocking
  _absoluteAngleNow(which motor, angle)
    Specifies an angle the servo should move to relative to the starting position
    Motor executes code immediately, without advancing the Arduino_nano_main.ino loop() until the motor has reached its final position
  _absoluteAngleNonBlocking (which motor, angle)
    Same as _absoluteAngleNow(), but non-blocking

## Slide 4: Core Functions in Folder “Arduino_nano_main”, cont.
Nano_servo_core_functions.ino
  _setNanoServoAngle(which servo, int angle)
    Sets the angle of an add-on ping sensor. Specify an angle 0 through 180 degrees. 0 degrees is all the way to the right
    The first variable passed to the function specifies which servo you want to talk to. Change which one you talk to in the Arduino_nano_main loop()
      This is helpful if you have more than one additional servo
Nano_ping_sensor_core_functions.ino
  _NanoDistanceTest(which ping sensor)
    Returns the distance in front of the ping sensor (what units??)
    The variable passed to the function specifies which servo you want to talk to. Change which one you talk to in the Arduino_nano_main loop()
      This is helpful if you have more than one additional ping sensor
IR_core_functions.ino
  Work later; specifies modes of robot
Bluetooth_core_functions.ino
  Work later; specifies modes of robot